## Slide 2: TA
Ayush Kumar.
Roll no: 20CS02008
Mobile No: 8875231058

## Slide 3: Problem-1
In CSMA/CD, what is the probability that a node chooses τ = 4 after the fifth collision from the back-off race? The result τ = 4 corresponds to a delay of how many seconds on a 10 Mbps Ethernet?
Minimum frame size on Ethernet = 512 bits = 64 bytes

## Slide 4: Solution
In CSMA/CD, after the 5th collision, the range of possible values will be {0,1,2,…31}. The size is 32. So the probability of choosing any particular value of τ = 1/32.
The probability that a node chooses τ = 4 is 1/32 = 0.03125.
For Ethernet, the amount of time a node waits is k x 512 bit times.
= (τ x 512/10*106) s = (2048/10*1000*1000) s
= 0.2 ms (approx.)
This is because at minimum 512 bits will be sent by any node, so it should wait at least that long to reduce collisions.

## Slide 5: Problem-2
A 2 km long broadcast LAN has 107 bps bandwidth and uses CSMA/CD. The signal travels along the wire at 2 x 108 m/sec. What is the minimum packet size that can be used on this network?
Hint: Relation is derived from the CSMA/CD technique used to avoid collision detection by the transmitter.

## Slide 6: Solution
Given:
Distance = 2 km, Bandwidth = 107 bps, Speed = 2 x 108 m/sec
frame size >= 2 * Bandwidth_delay_product
Propagation Delay (Tp) = Distance / Propagation speed
= 2 km / (2 x 108 m/sec)
= 2 x 103 m / (2 x 108 m/sec)
= 10-5 sec
Minimum frame size = 2 x Propagation delay x Bandwidth
= 2 x 10-5 sec x 107 bits per sec
= 200 bit or 25 Bytes

## Slide 7: Problem-3
A and B are the only two stations on Ethernet. Each has a steady queue of frames to send. Both A and B attempt to transmit a frame, collide and What is the probability that A wins the first back-off race?

## Slide 8: Solution
During the first transmission collision happens,
KA = 1 and KB = 1.
Now, Station A chose any backoff value from [0, 21 - 1] = [0, 1]
Similarly, Station B chooses a backoff value from [0, 21 - 1] = [0, 1]
Probability (A win Back-off race) = 1 / 4 = 0.25
Station A | Station B | Winner
0 | 0 | Tie
0 | 1 | A
1 | 0 | B
1 | 1 | Tie

## Slide 9: Problem-4
Suppose nodes A and B are on the same 10 Mbps broadcast channel, and the propagation delay between the two nodes is 325-bit times. Suppose CSMA/CD and Ethernet packets are used for this broadcast channel. Node A begins transmitting a frame and, before it finishes, node B begins transmitting a frame.
Can A finish transmitting before it detects that B has transmitted? Why or why not? (Assume t = 0 is when A starts transmitting)
Hint: Minimum frame size on Ethernet = 512 bits = 64 bytes
bit-time is the propagation delay in terms of bits.

## Slide 10: Solution
Suppose that at time t=0, node A starts transmitting the frame. The minimum time A can finish transmitting is t = 512-bit times.
● In the worst case, node B begins transmission at a time just before the first bit of node A arrives at node B before the propagation delay. So, node B starts its transmission at time t = 324-bit times.
● The propagation delay between node A and node B is 325-bit times. So, the first bit of node B arrives at node A at time =324 + 325 = 649-bit times. Therefore, in the worst case, B’s signal reaches A at t = 649 bit times = 0.06 ms approx.
● If the frame size <= 649 bits. Then, Node A will never detect that a collision is happened.
● If the frame size > 649 bits. Then, Node A gets to know about the collision.

## Slide 11: Problem-5
Imagine you are sending a file from your computer to a friend's computer over the Internet. The data travels through several connections between your computer and your friend's computer. Some of these connections are fast, and some are slow.
Which connection in the path between your computer and your friend's computer will determine how quickly the file can be sent?
A
B
R1
Rn

## Slide 12: Solution
The slowest connection in the path will determine the overall speed of the file transfer, which is called the throughput of the network.