## Slide 2: Name of the TAs
Raushni Kumari, Roll No: Mobile No:
Problem No YYY to Problem No YYY
2. Ayush Kumar
Problem No YYY to Problem No YYY
3. Vaibhav
Problem No YYY to Problem No YYY
4. Shanmukha Sharma
Problem No YYY to Problem No YYY

## Slide 3: Problem-1
Q. If the average number of collisions per unit time is 3 in a CSMA network, what is the probability that exactly 2 collisions will occur in a unit time?
Ans.
L2
L3

## Slide 4: Problem-1
Q. If the average number of collisions per unit time is 3 in a CSMA network, what is the probability that exactly 2 collisions will occur in a unit time?
Ans. Given:
Average number of collisions per unit time λ = 3
Number of exact collisions k = 2
Under a Poisson distribution with the expectation of λ events in a given interval, the probability of k events in the same interval is:
Ans = 0.224

## Slide 5: Problem-2
Q. If the expected number of packet arrivals in a time interval is 5, what is the expected number of arrivals in a time interval that is three times as long?
Ans.The expected number of arrivals would be
5×3=15

## Slide 6: Problem-2
Q. If the expected number of packet arrivals in a time interval is 5, what is the expected number of arrivals in a time interval that is three times as long?
Ans.

## Slide 7: Problem-3
Q. In a Slotted ALOHA system with 100 users, each user transmits a packet with a probability 𝑝 per slot. What is the expected number of successful transmissions in a single slot?
Ans.

## Slide 8: Problem-3
Q. In a Slotted ALOHA system with 100 users, each user transmits a packet with a probability 𝑝 per slot. What is the expected number of successful transmissions in a single slot?
Ans.
P(user i succeeds)=p⋅(1−p) N−1
Expected Number of Successful Transmissions:
Each of the 𝑁 users has the same probability of being the only transmitter. The expected number of successful transmissions is the sum of the probabilities of each user being the only one transmitting:
𝐸[Successful Transmissions]=𝑁⋅Probability (one user succeeds)
E[Successful Transmissions]=N⋅[p⋅(1−p) N−1]

## Slide 9: Problem-4
Q. In an ALOHA network, if the probability that a packet is successfully transmitted is 0.1 and there are 100 attempts, what is the expected number of successful transmissions?
Ans.

## Slide 10: Problem-4
Q. In an ALOHA network, if the probability that a packet is successfully transmitted is 0.1 and there are 100 attempts, what is the expected number of successful transmissions?
Ans. Probability of successful transmission for a packet 𝑃success =0.1
Number of attempts (or users) 𝑁=100 E[success]=100×0.1=10
The expected number of successful transmissions is calculated by multiplying the total number of attempts by the probability of success for each attempt. This is based on the principle that if each attempt is independent, the total number of successful transmissions follows from the probability of success for each attempt.
E[successful transmissions]=N×P success
E[successful transmissions]=100×0.1
𝐸[successful transmissions]=10